## Slide 1: Returnable Pallet Tracking
AIS → OEM / OES / AFM customers and back · Proposal for management approval · October 2026
Notes: Opening: one closed loop, every pallet known by ID. Ask for approval of pilot at Chennai and the hardware list on the last slide.

## Slide 2: Why: pallets leave by scan, but come back by count
15
plants dispatch returnable pallets to customers
0
pallets currently known by ID while at customer
Qty only
return recorded from a manual challan at the gate
?
pallets lost, aging or chargeable — not visible today
Today
Dispatch is scan-driven: pallet QR, green card, invoice QR, GCS QR
Return is count-driven: customer sends a manual challan, security records a quantity
Pallet IDs are identified only when the yard team scans at staging
No customer-wise holding, no aging, no reminder, no chargeable list
Pallets from other plants arrive mixed and cannot be processed
What AssetTrack changes
One barcode tag per pallet; every movement is a scan, validated by rules
Return Slip with QR replaces the manual challan (customer end or AIS gate)
Three-way reconciliation at the yard: ledger vs slip vs scan
Customer ledger by pallet ID with aging, reminders and chargeable list
Oracle EBS and GCS integrated: no double entry, gate fully system-controlled

## Slide 3: The closed loop in one picture
Dispatch left → right, return right → left. Blue = app, amber = control, dashed = Oracle EBS / GCS, red = customer, green = result.

## Slide 4: Revised process flow
Overview, dispatch and return in detail, controls and masters

## Slide 5: Revised end-to-end flow (v0.4)
Masters on top · DISPATCH lane: Pick List → EBS SO → dock scan → Pick List Control → challan → Challan Control → logistics approve → GCS out · RETURN lane: slip → IN gate → yard scan → reconcile

## Slide 6: Dispatch in detail: pick list, dock scanning, challan, gate
Dock out-ward scan & Pick List Control: unknown / retired tag, foreign pallet, not AVAILABLE and quantity checks — every rule also runs offline on the HHT
Challan (ORACLE / APP switch) → Logistics approve → GCS outward → OUT gate QR match. Mismatch = vehicle held; override only with supervisor PIN and logged

## Slide 7: Return in detail: return slip, IN gate, yard reconciliation
Return Slip: Mode A at customer end (scan + Bluetooth print, or push via API) · Mode B at AIS gate: B1 full scan, B2 quantity only (PENDING VERIFICATION)
IN gate scan creates GCS-IN · yard scans each pallet with the "accept other-plant" option · three-way reconcile → AVAILABLE / HELD / exception queue · close needs supervisor PIN if exceptions remain

## Slide 8: Four controls and how exceptions are handled
1
Pick List Control
Scanned count must equal pick-list qty; only same-plant AVAILABLE pallets; no duplicates
2
Challan Control
One challan per pick list, only after the dock scan is confirmed; source ORACLE or APP per plant/customer
3
Logistics Confirmation
Vehicle, transporter and challan approved in the app before any gate pass exists
4
Gate Control
OUT: GCS/challan QR must match an approved vehicle · IN: slip QR creates GCS-IN automatically
Exception queue at the yard
Short | on slip, not received → stays at customer, counted in reminders
Excess | received, not on slip → accepted, source customer corrected
Cross-customer | booked to X, returned by Y → moved between ledgers, flagged
Unknown tag | not in master → quarantine until identified / re-tagged
Damaged | photo, status DAMAGED, chargeable per customer master
Other-plant pallet | checkbox: accept → HELD + home plant alerted, or reject

## Slide 9: Masters, plant restriction and user control
Plant Master
15 plants · GSTIN · pallet & tag series · challan switch · other-plant default
Pallet & Tag Master
Pallet No permanent (never reused) · tag series independent, vendor batches of 400 · replace / retire · full tag history
Customer Master
Mail IDs, contacts · holding-days limit · reminder & escalation days · chargeable · return mode A/B · API key
Transporter Master
Codes, vehicles, contacts · selected on pick list and slip
Roles per plant (permission matrix in Admin)
Security – IN Gate · Security – Logistics / OUT Gate
Pallet Yard In-charge · FG Warehouse · QA / PDI · Logistics
Plant Admin (own plant users) · Master Maintenance (central)
Central Admin · Management (all-plant dashboards, read-only)
Every user is tied to one plant: data, scans and reports are filtered automatically
A plant cannot dispatch or assign another plant's pallets
Supervisor PIN for sensitive actions: close with exceptions, reduce qty, gate override, discontinue pallet
Lock after 5 failed logins · HHT device registration · immutable audit & activity log

## Slide 10: The solution
Architecture, contingency, actual screens, documents, integrations

## Slide 11: Architecture: Python · SQL Server · Android
Central server
FastAPI (Python) on IIS · SQL Server · 4 workers behind one port · separate integration worker so a slow Oracle never blocks a scan
HHT app (Android)
Rugged scanners or phones · offline-first outbox · camera or keyboard-wedge scanning · Bluetooth 2"/3" printer
Plant Edge Service
Portable Python service on the plant PC · takes over on the LAN if WAN / central server is down · forwards when back
Web console
Dashboard, masters, users, import, pick lists, slips, sync monitor, activity log, reports, Excel export
Integrations
Oracle EBS: SO post, challan · GCS: gate in/out · External customer API (API key) for Mode A push · retry queue
Security & audit
JWT login, plant scoping, role matrix, supervisor PIN, device block, activity logger on every action

## Slide 12: Production never stops: offline design and contingency
Failure | What keeps running | Normalisation after the fix
WAN / network down | Scans continue on HHT (local rules) or via plant edge service | Outbox replays in order; server de-duplicates
Central server down | Edge service serves the plant on LAN | Replay + reconciliation report; standby DB promoted
Oracle EBS down | Pick list saved SO PENDING; challan (APP mode) still prints; gate proceeds | SO posted by retry job every 5 min; number back-filled
GCS down | Manual gate-pass mode with challan QR + supervisor PIN | GCS created / closed in bulk when back; mismatch report
HHT lost / broken | Device blocked by admin; server knows its last heartbeat and pending count | Re-enter from paper slips; returned device outbox still accepted
Printer down | Print later; document stored | Reprint from any device or the web console
Rules in every mode: a truck is never held for the app · nothing is lost silently (UUID per event, two copies before acknowledgement) · central wins on conflict but never discards, it queues for review

## Slide 13: Server console: dashboard and dispatch control (actual screens)
Dashboard — plant-wise availability, customer holding & aging with OVERDUE flags
Pick lists — SO number from EBS, scanned count, challan, vehicle, GCS; action buttons by role
Return slips — Mode A (customer API) and B, GCS-IN, close with PIN
Printable A4 challan with AIS logo and QR

## Slide 14: Server console: reconciliation, sync and activity (actual screens)
Slip lines — declared vs received, DAMAGED / FOREIGN / EXCESS exceptions, resolve per line
Activity log — every action from web, HHT, external API; filters and Excel export
Sync monitor — devices, last seen, pending events, rejected / exception events, integration retry queue
Masters — plants, customers (with API key), transporters, tag batches; Excel import

## Slide 15: HHT app: home, dock scan, yard reconciliation
Role-based tiles; status bar: ONLINE/OFFLINE + pending
Count vs pick-list qty; rule failures beep in red
Received / short / excess; other-plant & damaged switches

## Slide 16: HHT app: return slip, sync, OUT gate, thermal challan
B1 scan / B2 qty; prints 2 copies with QR
Outbox, offline docs, my activity
QR must match approved vehicle
3" thermal challan with logo & QR

## Slide 17: Documents generated by the system (actual output)
Delivery challan — returnable pallets (Rule 55): consignee, transport, pallet list with tags, return period, signatures, QR
Return slip — customer challan, vehicle, driver, declared vs received, exceptions, GCS-IN
Challan source switch
APP mode: numbered from the plant series, printed A4 and 3" thermal, posted to EBS as reference. ORACLE mode: challan number pulled from EBS and printed in the same layouts. Both carry the QR scanned at the OUT gate and by the customer.

## Slide 18: Integrations and the customer end
Oracle EBS
Sale order posted by API when a pick list is created (SO number stored) · returnable challan from EBS when switch = ORACLE · pallet liability visible in ERP
GCS (internal gate system)
Outward pass auto-created on logistics approval, approved on gate QR match · inward pass created from the return-slip QR, closed with the received quantity
Customer end (outside AIS network)
External API with per-customer key, published through DMZ: holding list, validate tags, push return slip with pallets, vehicle and their challan · phone + Bluetooth printer kit
Reminders, aging and management reports
Nightly job: days at customer vs Customer Master limit → reminder mail with pallet list (To / CC from master), escalation to sales, chargeable list
Dashboards: plant-wise availability, customer holding by age bucket, overdue pallets, exception queue, tag stock
Reports: pallet transaction history, tag change history, audit log, activity log — all exportable to Excel

## Slide 19: Roadmap
Phases, timeline and what each phase delivers

## Slide 20: Roadmap: six phases from pilot to all 15 plants
Phase | Scope | Duration | What is built | Outcome
0 | Discovery & spec freeze | 2 wks | State machine, Return Slip & challan formats, API contracts (EBS SO, Oracle challan, GCS), master data from 15 plants, pallet census plan | Frozen spec, opening-stock approach
1 | Core + masters + yard | 3 wks | Server on IIS/SQL Server, masters & roles, Excel import, tags on pallets (census), HHT offline core, yard in-ward scan, sync monitor | Plant pallet inventory becomes real
2 | Dispatch validation | 3–4 wks | Pick list → EBS SO post, dock scan, Pick List Control, challan switch (ORACLE/APP), logistics approve, OUT gate | Every outgoing pallet known by ID and customer
3 | GCS integration | 2 wks | GCS outward auto-created and approved on gate QR; GCS inward from return-slip QR; manual gate-pass fallback | Gate fully system-controlled both ways
4 | Return module | 3–4 wks | Return slip Mode A (customer API / kit) and Mode B (gate), three-way reconciliation, exception queue, plant edge service | Returns tracked by pallet ID; no manual challan
5 | Analytics & rollout | 3 wks + rollout | Reminder mails, aging & chargeable list, dashboards, day-end check; rollout one plant every 2 weeks | Management visibility across the network
6 | Add-ons | later | Green-card API check at production, HMIL PDI hook, customer self-service portal, Vehicle Live Tracker link | Closed loop from manufacturing to customer portal
Status today: Phase 1–2 software (server v1.3, HHT v1.3) and Phase 4 return module are built and tested with sample data; integrations run in STUB mode until EBS / GCS endpoints are shared.

## Slide 21: Timeline: Chennai pilot live in Q4, network rollout through 2027
Oct 26
Nov 26
Dec 26
Jan 27
Feb 27
Mar 27
Apr 27
May 27
Jun 27
Phase 0 · Spec freeze
Phase 1 · Core, masters, yard
Phase 2 · Dispatch validation
Phase 3 · GCS integration
Phase 4 · Return module + edge
Chennai pilot go-live
Phase 5 · Analytics, reminders
Rollout wave 1 · AAU, PUN, TAL
Rollout wave 2 · RKE, BWL + 4 plants
Rollout wave 3 · remaining plants
Phase 6 · Add-ons & portal
Assumes EBS and GCS endpoints available by mid-November and tags fixed on Chennai pallets during Phase 1. One plant goes live every two weeks once the pilot is stable.

## Slide 22: Pilot plan and what each plant needs
Done
Server v1.3, HHT app v1.3, masters template, flows & documents
Phase 0 · 2 wks
Spec freeze with ERP & GCS teams: SO API, challan, GCS contracts; master data from 15 plants
Phase 1-2 · 4 wks
Chennai pilot: masters, tags on pallets, dock scan, challan, logistics, gate · "pull the cable" test
Phase 3-4 · 4 wks
GCS live, Oracle live, return slips with HMIL (Mode A), yard reconciliation
Phase 5 · 3 wks
Reminder mails, dashboards, edge service, day-end check
Rollout
One plant per 2 weeks: AAU, PUN, TAL, RKE, BWL … 15 plants
Hardware per plant (indicative)
2–4 rugged Android HHTs (existing scanners can be reused)
1 HHT with built-in printer or 1 Bluetooth 3" printer at the IN gate
Barcode tags: ~400 per batch per plant (vendor printed)
Plant PC for the edge service (no admin rights needed)
Central (IT)
Windows Server with IIS · SQL Server (Standard or Express for pilot)
DMZ rule for the external customer API only
Oracle SOA endpoints for SO & challan · GCS API or DB access
Mail relay for customer reminders

## Slide 23: Approval requested
1
Approve the Chennai pilot
Phase 0–2 start, 6 weeks, with HMIL as the first Mode A customer
2
Nominate owners
ERP (SO/challan API), GCS team, plant logistics & security leads, Master Maintenance team
3
Sanction hardware
HHTs, gate printer and tag batches for Chennai; central IIS / SQL Server instance
4
Agree the policy
Customer holding-days limits, chargeable rule and write-off after escalation
Outcome: every AIS pallet tracked by ID from plant to customer and back · live availability · customer accountability · no double entry